## Slide 1
DISPLACEMENT DEVICE FOR ION EXTRACTION IN LXe
Ryan Elmansali
Supervisor: Dr. Razvan Gornea
CAP 2023

## Slide 2: Neutrinos
Neutrinos come in 3 "flavours": νe, νμ, ντ
They change flavour as they propagate (neutrino oscillation)
Neutrinos are massive!
Absolute mass and ordering (mass hierarchy) remains unknown.

## Slide 3: Neutrino-less Double Beta Decay
0νββ
Neutrino-less: 2n 2p + 2e-
Only possible if neutrinos are Majorana
Want to observe 0νββ since Decay rate is related to neutrino mass
2νββ

## Slide 4: Barium Tagging
Identification of the Ba daughter in Xe neutrino-less double beta decay
Ba ion collection occurs at the decay location
Rejects all radioactive backgrounds but not 2νββ
Tagging has many steps, beginning with the physical collection of a single Ba+ in LXe
136Xe 136Ba + 2e-
Identify this!

## Slide 5: Ion extraction at Carleton
Dissolved in LXe
Distinctive signature detected by TPC; location determined for extraction
Ion extracted by capillary, transported to PIPS detector
with high efficiency
Decay identified by energy deposited in PIPS
Wobblestick
Capillary probe
TPC
Displacement device
PIPS detector chamber

## Slide 6: Displacement device
WS40 manipulation moves probe tip
Ion extraction requires fast, controlled and precise manipulation of the probe tip
Developed a 2-stage, stepper motor driven device which allows for positioning accurate to 0.1mm in each axis at speeds up to 15 mm/s
X-Y Stage
Insert/Retract Stage

## Slide 7
X-Y stage sets angle around WS pivot
Third motor controls insertion/retraction through openings in TPC cathode

## Slide 8: Optimal Motor Kinematics Delivery
Developed software that delivers fast and smooth motion
User need only to provide destination coordinates along with an execution time
Firmware achieves this by calculating necessary delay time between steps in real time
Coordinates passed to software after event reconstruction

## Slide 9: Performance
3D motion tests done by using an electronic track pad + pen touching specific points on a plane
Physical positions on pad corresponds to cursor location on screen in pixels
Compare programmed destination points with positioning feedback from track pad
Dial indicator testing on each individual axis shows motion is faithful to 0.01 mm

## Slide 10: Star Test
Touched ten corners of a star
All points touched are at desired position within resolution of track pad (0.11 mm)
Repeat 3 consecutive times

## Slide 11: ION Collection efficiency
Likelihood that a certain event will
be collected by capillary probe ​
Considers:​
  Accessibility of event position​
  Time to reach event position (3.1 m radioactive ion lifetime)​
  Random walk of ion after detection​
  Volume collected by probe ​

## Slide 12: ION Collection Efficiency
Monte Carlo of 1000 points randomly placed inside TPC
Collection process simulated 2500 at each point
Escape and radioactive decay are the loss mechanisms
Low efficiency points: hard to access with probe tip, won’t attempt extraction
Notes: Plot shows collection efficiency of simulated points randomly distributed within TPC

## Slide 13
Only 15% of points within TPC are directly accessible by probe tip → allow for a 2.5, 5 or 7mm lateral deviation
90% of points inside TPC are accessible within 8 mm of probe tip
Trade-off individual event collection efficiency to greatly increase total accessible events

## Slide 14
Must enter TPC through one of the cathode holes
Probe has an effective thickness of ¼ inches in diameter
High, outer-ring points are not reasonably reached

## Slide 15: Conclusions + Future work
Developed programmable 3D motion device capable of delivering fast, smooth and precise motion
Monte Carlo results show how we can make the most out of our limiting geometry for ion collection
Full targeted extraction later this summer!

## Slide 16: Thank you!
Supervisor: Dr. Razvan Gornea
Collaborators: Dr. Robert Collister, Raad Shaikh

## Slide 17: Extras

## Slide 18: Time Projection Chamber (TPC)
Particle detection device with 3D event reconstruction
Gas or liquid sensitive volume (often inert noble elements)
High energy particles ionize medium
E-field drifts e- to charge collection plane (anode)
PMTs for light collection to detect scintillation photons
Z position reconstruction comes from e- drift timing
Grid segmentation of wires allows for X-Y reconstruction
e-
e-
e-
e-
e-
e-

## Slide 19: Track Pad Calibration
Each fit is a calibration function that transforms points on track pad to motor coordinate system
Slopes of each function represents the pixels to mm conversion factor for each axis respectively
mx-axis ≠ my-axis pixels are not square!

## Slide 20
Nonlinear relationship between lateral deviation and accessibility
7mm clearly is taking this alleviation too far
Max out most likely at 5mm